## Slide 1
Lean Manufacturing
Mel Wendell – Mountain Pointe High School

## Slide 2: Course Agenda
Welcome and Background Information
1st round of Simulation (ENGR Catamaran)
Lean Manufacturing
Lean Principles
2nd round of Simulation (ENGR Catamaran)
Lean Manufacturing Building Blocks
Closure

## Slide 3: Round 1: ENGR CATAMARAN
Welcome – Team Introductions and Company Names
Departments
  Hull Assembly (2)
  Rudder and Sail Joint Assembly (2)
  Sail Assembly (1)
  Final Assembly (1)
  Quality Control (1)
Goals
    3 Catamarans in 9 minutes
    100 % Quality
Discussion
(#) Recommended students per group.
Notes: Provide time for introduction of school and what they teach. After Departments, pass out the parts sheet and the work instructions. Make sure they do not read the instructions until they are told to do so!!!

## Slide 4: Lean
“A systematic approach to identifying and eliminating waste (non value-added activities) through continuous improvements by flowing the product at the pull of the customer in pursuit of perfect.”
In Other Words:
Give the customer what they want, when they want it and don’t waste anything.

## Slide 5: Principles for Lean Manufacturing

## Slide 6: Identify Value
Any activity that changes the form or function of the product.
  Ex – Machining, Fab, Assembly, Molding
Done right the first time. (Quality & Delivery)
Activities the customer is willing to pay for.
Value-Added (5%)

## Slide 7: Identify Value
Any activity that does not change form or function or is not necessary.
  Ex – Sales, Production Control, Purchasing, HR, Shipping/Receiving, QC, Accounting, etc.
These activities should be eliminated, simplified, reduced, or integrated.
Non Value-Added (95%)

## Slide 8: Identify Value
Any activity that does not change form or function BUT is necessary.
  Ex: cleaning/packaging, debur, inspection, etc.
These activities should be simplified, reduced, or integrated.
Non Value-Added BUT Necessary

## Slide 9
Map the Value Stream

## Slide 10
Waste is “anything other than the minimum amount of equipment, materials, parts, space, and worker’s time which are absolutely essential to add value to the product.”
- Shoichiro Toyoda President, Toyota
Waste = Non Value Added

## Slide 11: Why Focus on Waste ?
Waste is a symptom signaling Time & Money is trapped in the process
Waste is a systemic flaw affecting people, materials, machines, and/or information
Recognizing waste can lead to identifying the root cause of problems and saving Time & Money

## Slide 12: Lean = Eliminating Waste
Defects
Overproduction of work in process
Waiting
Non–value-added processing
Transportation of materials & equipment
Inventory Excesses
Motion
Employees Underutilized
Typically, 95% of all lead time is non–value added!

## Slide 13: Motion
Any movement of people or machines that does not add value to the product or service
Causes of motion waste:
  Dis-organized work space
  Inconsistent work methods
  Inefficient facility or cell layout
  Insufficient training or supervision
  Inadequate tools or supplies at workstation
Searching
How long would you look?

## Slide 14: Organization
Better
Limits waste of motion

## Slide 15: Creating Flow
Linking of manual and machine operations into the most efficient combination to maximize value-added content while minimizing waste
Hull
Rudder & Sail Joint
Sail
Final

## Slide 16: Step 1: Group Products
Products with similar processing requirements are grouped into product families
Processing Steps
 | Hull | Steering | Rudder & Sail Joint | Sail | Test
Catamaran | × |  | × | × | ×
Sail Boat | × | × | × | × | ×

## Slide 17: Step 2: Establish Cycle Time
Demand = Customer order or Production order
Work Time = Quoted or Established production time
Cycle Time =
9 min
3 catamarans
= 3 min/catamaran
Goal: Produce to Demand
Work Time
Demand
Cycle Time =

## Slide 18: Step 3: Review Work Sequence
Observe sequence of tasks each worker performs
Break operations into observable elements
Identify value-added versus non-value-added.
Eliminate or minimize
non-value-added
Study machine capacity,
cycle times and changeover
times
Round 1 Sequence Times
Hull 120 sec
Rudder & Sail Joint 75 sec
Sail 30 sec
Final Assembly 20 sec
Inspection 20 sec

## Slide 19: Step 4: Combine Work / Balance Process
Cycle Time = 3 min
Unbalanced Line
Balanced Line
Chart: Traditional Manufacturing
| Hull | Rudder | Sail | Assembly | Inspection
Traditional Manufacturing | 120 | 75 | 60 | 20 | 20
Chart: Lean Manufacturing
| Hull | Rudder | Sail | Inspection
Series 1 | 75 | 45 | 30 | 20

## Slide 20: Round 2: ENGR CATAMARAN
Departments
  Hull Assembly (3)
  Rudder and Sail Joint Assembly (2)
  Sail Assembly (1)
  Quality Control (1)
Goals
    3 Catamarans in 9 minutes
    100 % Quality
Discussion

## Slide 21: Lean Building Blocks
Quick Changeover
Standardized Work
Batch Reduction
Quality at Source
5S System
Visual
POUS
Cellular/Flow
Pull / Kanban
Continuous Improvement
Value
Stream
Mapping

## Slide 22: Questions?
Presenter: Melissa Wendell
Session Name: Lean Manufacturing
E-mail: mwendell@tempeunion.org
Notes: Don’t forget the survey!!!

## Slide 23
Thank You.
Notes: 23